## Slide 1
COEN 210 Project
Santosh Nanduri
Akshay Parkala
Parth Shah

## Slide 2
1
2
4
Datapath and Control
Performance Analysis
Instruction Set
Contents
3
Super Instruction

## Slide 3
01
Instruction Set

## Slide 4
Constant
7 bits
RS2
7 bits
RS1
7 bits
RD
7 bits
OPCODE
5 bits
Instruction Format

## Slide 5
10 110
Opcode
Instruction
Syntax
Description
INC
DEC
AND
OR
NOR
10 001
INC
Instructions – R type
INC x1,x2,x3
x1 = x2 + x3
10 010
DEC x1, x2, x3
x1 = x2 - x3
AND x1, x2, x3
x1 = x2 & x3
NOR x1, x2, x3
x1 = x2 nor x3
10 011
10 101
OR x1, x2, x3
x1 = x2 or x3

## Slide 6
Opcode
Instruction
Syntax
Description
LOAD
STORE
00 011
Instructions – Data Transfer
LOAD x1, x2
rd = mem[rs1]
10 001
STORE x1,x2
mem[rs2] = rs1
SD rs1, rs2

## Slide 7
Instructions – Immediate
Opcode
Instruction
Syntax
Description
INCI
ANDI
00 001
INCI x1, x2, 100
x1= x2 + 100
00 100
ANDI x1, x2, 100
x1 = x2 & 100

## Slide 8
Instructions – Branch and Jump
BEQ x1, x2, 1000
if x1 = x2 =>
PC = PC + 1000
11 011
jal rd, imm
PC = 2000
x1 = PC + 4
Opcode
Instruction
Syntax
Description
BEQ
JAL
11 010
JAL x1, 2000
JALR x1,24(x2)
PC = x2 + 24
x1 = PC + 4
11 001
JALR

## Slide 9
02
Datapath and Control

## Slide 10
M
U
X
4
ADDER
[4:0]
RS1 RS2 PC PC+4 Rd
Read Addr 1
Read Addr 2
Read Data 1
Read Data 2
Wrt Addr
Wrt Data
M
U
X
M
U
X
Shift
Left 1
Data
Mem
Read Addr
Wrt Addr
Wrt Data
Read Data
JBU
M
U
X
PC+4
Rd
M
U
X
Buffer Flush
ADDER
PC
INST
MEM
REG FILE
CONTROL
IMM
M
U
X
4
M
U
X
PC
Read Data 1
M
U
X
Imm
MemW
MemR
AdSrc1
AdSrc2
Branch
Jump
ALU
ALUSrc
Forwarding Unit
PCWrt
RegW
FwdCntrl

## Slide 11
JBU
JBU
M
U
X
Branch
Jump
Zero Flag
PC Src
Buffer Flush
Jump and Branch Unit
PC + 4
Normal: Branch = 0 & Jump = 0
Branch Not Taken: Zero Flag = 0 & Jump = 0
00
Immediate
Jal: Branch = 0 and Jump = 1
01
PC + Immediate
Branch Taken: Branch = 1, Zero Flag = 1 and Jump = 0
10
Reg + Immediate
Jalr: Branch = 1 and Jump = 1
11
IF/ID and ID/EX Flush
Both these registers have to be flushed when branch is taken or unconditionally jumped
Notes: S1: (Branch&ZeroFlag) if Jump=0 else Branch
S0: Jump

## Slide 12
Instructions – Emulation
Instruction | Emulation
BEQ x1, x2, 1000 | BEQ x1, x2, 1000
JAL x1, 2000 | JAL x1, 2000
JALR x1,24(x2) | JALR x1,24(x2)
ADDI x1, x2, 100 | INCI x1, x2, 100
ANDI x1, x2, 100 | ANDI x1, x2, 100
ADD x1,x2,x3 | INC x1,x2,x3
SUB x1, x2, x3 | DEC x1, x2, x3
AND x1, x2, x3 | AND x1, x2, x3
OR x1, x2, x3 | OR x1, x2, x3
NOR x1, x2, x3 | NOR x1, x2, x3
SD x1, imm(x2) | ADDI x2, x2, imm STORE x1, x2 DECI x2, x2, imm
LD x1, imm(x2) | ADDI x2, x2, imm LOAD x1, x2 DECI x2, x2, imm

## Slide 13
03
Super Instruction

## Slide 14
Constant
n
RS2
7
RS1
7
RD
7
OPCODE
11111
Instruction Format
ADDMTX
x7
n
Forwarding
Instead of fetching the partial sum from the register each and every cycle, we take advantage of the forwarding unit and forward the memory and ALU outputs during every cycle.

## Slide 15
Forwarding Unit
FWD Control Signal | Function
1 (only Super instruction) | Forward RegWrtOutput and EX/WB.MemoryOutput to MUX1 and MUX2 respectively
0(All other instructions) | Similar to RISC-V

## Slide 16
CYCLE | ALUOp | ALUSrc | MemR | MemRSrc | MemW | AdSrc1 | AdSrc2 | RegW | RegWSrc | PCWrt | Jump | Branch | Fwd
1 | 000 | 0 | 1 | 0 | 0 | 1 | 01 | 1 | 01 | 0 | 0 | 0 | 1
2 to n | 001 | 0 | 1 | 1 | 0 | 1 | 10 | 1 | 01 | 0 | 0 | 0 | 1
n + 1 | 001 | 0 | 0 | X | 0 | 0 | X | 1 | 01 | 1 | 0 | 0 | 1
Control Signals

## Slide 17
Calculate Next Element Address
Instruction Fetch
Instruction Decode
Fetch Element
Accumulate Previous Element
Pipeline Process
1st Cycle
2nd Cycle
n+1 Cycles
Calculate Next Element Address
n+4th Cycle
Writeback Sum
Calculate Next Element Address
PC
As long as the Super instruction is in the pipeline, the PCWrite has to be deasserted so that the next instruction does not enter the pipeline

## Slide 18
04
Performance Analysis

## Slide 19
Constant
n
RS2
7
RS1
7
Performance without Loop Unrolling
INCI X6, X0, 1000 // X6 has base address of the array
INCI X5, X5, 0 // X5 maintains the additions
INCI X4, X0, N // X4 has number of elements in the array
LOOP: LOAD X7, X6
INCI X6, X6, -4
INC X4, X4, -1
INC X4, X5, X7
DIFF X4, X0 LOOP
NOP
NOP
Instruction Count : 3 + 7N
Cycle Count = 4 + (3 + 7N - 1) = 6 + 7N
CPI = #Cycles / #Instructions = (6 + 7N) / (3 + 7N) ≈ 1
Clock Period = 2ns
Total Executions time = CPI * Cycle Count * Clock Period
= (1 * (6 + 7N) * 2) ns
= (12 + 14N) ns
Notes: Assuming the loop is unrolled 4 times. Every time a loop is unrolled, we can reduce the number of instructions required by 2. So, we are reducing 8 instructions in total because the loop is unrolled 4 times.

## Slide 20
Constant
n
RS2
7
RS1
7
Performance with Loop Unrolling
INCI X6, X0, 1000 // X6 has base address of the array
INCI X5, X5, 0 // X5 maintains the additions
INCI X4, X0, N // X4 has number of elements in the array
LOOP: LOAD X7, X6
INCI X6, X6, -4
INCI X5, X5, X7
LOAD X7, X6
INCI X6, X6, -4
INC X5, X5, X7
LOAD X7, X6
INC X6, X6, -4
INC X5, X5, X7
LOAD X7, X6
INC X6, X6, -4
INC X4, X4, -4
INC X4, X5, X7
DIFF X4, X0 LOOP
NOP
NOP
Instruction Count : 3 + (16n/4) = 3 + 4N
Cycle Count = 4 + (3 + 4N - 1) = 6 + 4N
CPI = #Cycles / #Instructions = (6 + 4N) / (3 + 4N) ≈ 1
Clock Period = 2ns
Total Execution time = CPI * Cycle Count * Clock Period
= (1 * (6 + 4N) * 2) ns
= (12 + 8N) ns
Performance improvement using Loop Unrolling = Execution time without Loop Unrolling∕ Execution time with Loop Unrolling
= (12 + 14N) / (12 + 8N) ≈ 1.75
Notes: Assuming the loop is unrolled 4 times. Every time a loop is unrolled, we can reduce the number of instructions required by 2. So, we are reducing 8 instructions in total because the loop is unrolled 4 times.

## Slide 21
Constant
n
RS2
7
RS1
7
Performance with Super Instruction
ADDMTX X7, N
Instruction Count : 1
Cycle Count = 5 + N
CPI = #Cycles / #Instructions = (5 + N) / (1) = 5 + N
Clock Period = 2ns
Total Executions time = CPI * Cycle Count * Clock Period
= (1 * (5 + N) * 2) ns
= (10 + 2N) ns
Performance improvement using Super Instruction = Execution time with Loop Unrolling ∕ Execution time with Super Instruction
= (12 + 8N) / (10 + 2N) ≈ 4
Notes: Assuming the loop is unrolled 4 times. Every time a loop is unrolled, we can reduce the number of instructions required by 2. So, we are reducing 8 instructions in total because the loop is unrolled 4 times.

## Slide 22
Thank You